## Slide 1
200. Basic Trail Design
Notes: For curious trail workers who want to understand why so many trails are in bad shape because of how they were made. Learn how better design and layout makes trails more sustainable and less prone to erosion. Introduction to different trail design standards appropriate for different kinds of trails. This class is for anybody interested in these topics, but students with some trail building and maintenance experience will benefit the most.
First we will discuss Trail Planning, then Trail Layout, then Flagging. The afternoon portion of this class is a field exercise using clinometers and flagging a hypothetical new trail.

## Slide 2: Trail Planning Concepts
How The Planning Process Affects Design
Major and Minor Control Points in Trail Corridors
The Importance of Reconnaissance
How to Design for Land Capability, Aesthetics, and Safety Concerns
The Need for Resource Specialists Review Before Flagging a Trail Alignment

## Slide 3: Hikers and Backpackers
Identify the Trail User
Notes: The first factor in Trail Planning is determining the user type for which the trail is intended. Each user type needs a trail of an appropriate surface, grade (steepness), and clearance.

## Slide 4: New or Altered Trails May Need to Comply with ADA
New Outdoor Access Guidelines for Trails
User Types Dictate
Design Criteria

## Slide 5
Equestrians

## Slide 6
Mountain Bikes

## Slide 7
Determine Specifications & Standards – Based on User Group, Classification and Season of Use
Notes: The land management agency (eg, USFS) has sets of trail standards based on user type, trail class, and season of use. These may vary regionally. Make sure to consult with your local unit on the right set of standards for your trail.
Discuss the usefulness of a trail classification system for planning trail maintenance and providing different trail experiences.

## Slide 8
Land Unit Trail Plan
Notes: Trail planners need to research whether the area they have in mind for the trail already has land management plans in place, for example, plans pertaining to recreation, wildlife, forestry. . .

## Slide 9
Notes: or watersheds. Additionally, some pieces of Federal land have special Congressional designations such as Wilderness Area, Wild and Scenic River, or National Scenic Trail. Such lands, including the Pacific Crest National Scenic Trail, have special management plans that further guide trail planning and design.

## Slide 10
Topographic Maps
Topographic Maps
Notes: The next step in Trail Planning is to obtain a detailed Topographic Map of the area. (Show students briefly how to read contour lines: eg, lines closer together means steeper hillside, etc).

## Slide 11: Identify Control Points
Control Points are areas that the Trail Corridor NEEDS to go to (positive) or miss (negative)
Major control points are identified BEFORE on-the-ground reconnaissance
Notes: Using the topo map, begin to identify Control Points. Major control points can usually be identified on the map, before on-the-ground reconnaissance. Examples of major control points in following slides.

## Slide 13
Major Control Points
Rivers or Bodies of Water
Notes: Positive control points are highly desirable places by which they want the trail to pass. Examples include a trailhead location with adequate parking, stream crossings for affordable bridges (narrow and high-banked) or safe fords (shallow and firm), scenic viewpoints, and side-hill terrain with durable soils on which to build a sustainable trail.

## Slide 14
Major Road or Highway Crossings

## Slide 15
Large Wildlife Management Areas
Notes: Negative control points are places that should be avoided such as swamps, rock slides, avalanche chutes, critical wildlife habitat, and fragile archeological sites, among many others.

## Slide 16
Property Boundaries, In-holdings, Easements

## Slide 17
Get the Big Picture
Try to get a High Visual Overview of the Shorter Corridor Unit
Notes: Major control points not obvious on maps can become evident with a big picture overview, that is, a high visual overview of the shorter corridor unit. Designers may be able to view the target area from the opposite side of a valley, from a body of water, or from detailed aerial photos (eg, Google Earth).

## Slide 18
High Prominent Ridges, Lookouts

## Slide 19: Vegetation is an indicator of soil types and land capability
Notes: Aerial photos can reveal different vegetation types, indicative of different soil types.

## Slide 20
http://earth.google.com/

## Slide 21
Reconnaissance
  Ground Checking the Trail Corridor, from one Major Control to Another
  Identification of Minor Control Points
Notes: Now that you’ve identified a very rough trail corridor based on researching land management plans, maps, and photos, it’s time to get out on the ground and check it out.

## Slide 22: Minor Control Points
Features in the Trail Corridor that will Influence the Alignment of the Trail
Discovered and Worked Around During On-the-Ground Reconnaissance
Notes: During reconnaissance, designers establish minor control points. These may cause minor shifts in the trail alignment, but won’t change the overall route. Examples to follow. . .

## Slide 23
Rock Outcrops
Notes: Examples include rock outcrops, springs/seeps, big trees, and rock slides/debris flows. Designers keep track of rough grades between control points with a clinometer. Reconnaissance also allows designers to determine an alignment that highlights the natural aesthetics of the area.

## Slide 24: Stream Crossings Fully Investigate for Proper Trail Alignment
Notes: What’s wrong with this picture? The stream moved!

## Slide 25: Large Trees are Minor Controls
10’
Notes: Notice how much the trail grade would be affected if it were aligned over top of the tree. To produce the most graceful and sustainable tread alignment, decisions about which way to go around minor controls need to be considered before flagging begins.

## Slide 26: Scarps
Slope Instability
Notes: On the ground reconnaissance reveals smaller areas of instability that may need to be avoided.

## Slide 27: Debris Flows

## Slide 28: Look Hard Vegetation Hides Old Slides

## Slide 29: Tilted Trees

## Slide 30: Land Capability: Soils Soils Range From Rock to Sand Trail Grade Depends on Use, Soil, and Season of Use
Notes: Reconnaissance is also the time for careful assessment of land capabilities. Soil type and vegetation are clues as to whether or not the terrain is suitable for a trail. Best are durable soils on hillsides that can sustain a full bench with good outslope (more on these topics below). A varied matrix of good material, (eg, clay-sand, and angular gravel), will compact and keep soil moisture content, sustaining steeper grades and heavier use.

## Slide 31: Sandy Soils Appear Stable
Notes: And they might be stable, at flat grades.

## Slide 32
Sandy Soils Appear Stable
Until Slight Grades
Notes: However, with even a slight grade change, soils that are primarily sand won’t hold up.

## Slide 33
Notes: Look at how much this sandy trail has gullied.

## Slide 34: Clay Soils Lose Structure with Moisture
Notes: “Pure” clay makes a good trail surface only when dry! However, some clay mixed in with other soil types, is a good thing.

## Slide 35: Angular Fractured Rock Shales Durable Material Matrix

## Slide 36: From Least to Most Durable: (for trails with grade) Sand Silt Loam Clay Gravel Shale or Angular Rock
Notes: Soils are almost never purely one of these, but a mix.

## Slide 37: A Good Material Matrix Will Compact and Keep Soil Moisture Content Sustains Grade and Heavy Use
Notes: A mix of soils with various particle sizes and a bit of fine binder material (eg, clay), produces a durable tread surface.
During reconnaissance, aim to align your corridor upon the most durable surfaces.

## Slide 38
During Reconnaissance
Keep Track of Grades With Clinometer
Define a Rough Trail Corridor & Break it Into Smaller Segments
Notes: After reconnaissance, designers plot a rough trail corridor, either on a map, with GPS, or on the ground with loose flagging.

## Slide 39
When Trail Corridor Is Narrowed Sufficiently
Get Resource Specialists Involved on the Ground
Notes: Then it is time to call in resource specialists for their on-the-ground surveys. A trail that is to be built on any Federal land must follow guidelines of the National Environmental Policy Act (NEPA) to be sure that trail construction and use do minimal damage to fragile ecological, historical, or archeological resources.

## Slide 40: Consultation and Surveys on Sensitive, Threatened and Endangered Wildlife Species and Plants
Notes: This involves the analysis by a variety of specialists, including botanists, wildlife and fisheries biologists, and archeologists, among others. If the specialists reveal sensitive areas that a trail could disrupt, designers then consider these major control points, and reassess the proposed route.

## Slide 41: Hydrologist Review of Stream Crossings

## Slide 42: Archaeologist Cultural Survey

## Slide 43: Trail Planning Process
Set User Type and Standards
Literature Search, Maps, Photos
Identify Major Control Points
Broad Corridor Proposal
Field Check by Reconnaissance
Negotiate Minor Control Points
Assess Soil Types and Land Capabilities
Rough Map Control Points and Trail Corridor
Bring In Resource Specialists for Review
Now Final Alignment Can Begin

## Slide 44: Trail Layout

## Slide 45: Trail Layout Concepts
Understand Hydrologic Influences of Trail Alignments
Determine the Maximum Sustainable Linear Grade
Measure Linear Grades Between Control Points
Learn the Process of Flagging the Trail Alignment

## Slide 46: Water is the Most Influential Factor in Designing and Laying Out Trails
Notes: What is happening on these trails? Water is flowing down the middle of the trail, causing erosion and disrupting the natural hydrological pattern of the hillside. This is what you do not want.

## Slide 47
Trail Anatomy:
Sidehill Tread
Notes: Ideal sidehill tread is outsloped, and has no slough or berm. In the last slide, if the berm were removed and the outslope restored, water would not have diverted onto the trail.

## Slide 48: Curvilinear Alignment (Opposite of Fall Line) Makes the Trail Basically Perpendicular to Natural Sheet Runoff
Notes: In a perfect trail world, water from rain, melting snow, and seeps, sheet flows down a hillside and encounters a trail with good outslope and no berm-- it gently crosses the trail and continues down the hillside without causing any erosion of the trail tread.
Water naturally goes down the fall line. The Fall line is the fastest way down the hill. If a trail goes straight up the fall line, there is no way to drain the water off of it.

## Slide 49: Following the Contour of the Land Facilitates Natural Sheet Drainage Across the Trail
Notes: Curvilinear alignment means following the contour lines, at gentle grades. A fall line trail, on the other hand, would intersect the contour lines.

## Slide 50: Curvilinear Layout Requires Closely Following the Landform Pulling in and out of all Swales and Crenulations

## Slide 51: Natural Runoff Patterns
Notes: Runoff that begins as uniform sheetflow concentrates into naturally-formed drainages (aka draws, swales) which get bigger and bigger as they descend the hill.

## Slide 52: Hillside Hydrology
Notes: Same natural runoff pattern shown on a topo map.

## Slide 53: Modified Runoff Pattern
Notes: Now look what happens when we add a trail (yellow line). Water is diverted onto the trail. We’ve changed they hillside’s hydrological patterns. The small red lines indicate waterbars installed arbitrarily to drain the trail. This is not ideal. Notice what is happening below. Some areas (yellow circles) are drier than they used to be. Other areas (orange circles) are receiving too much water.

## Slide 54: Interception and Diversion of Sheetflow
Notes: Here is the same phenomenon on a topo map.

## Slide 55: When Water Accumulates on the Trail and is Arbitrarily Drained Off It Creates Erosion Below the Drain Point
Notes: What’s wrong with the placement of this waterbar? It drains onto a ridge.

## Slide 56: Some Diversions Combine Two Drainages, Dewatering One and Destabilizing the Other

## Slide 57: Vegetation and Wildlife Communities Below are Affected by Changing the Amount of Water They Receive
Notes: We build trails to take us out into landscapes we want to enjoy in their natural state. But if our trails are changing the landscape’s hydrological patterns, we are impacting that landscape. Therefore, we need to ensure our trails are designed well and continue to drain properly– it is a Leave No Trace practice!
The best way to protect trails from typical erosion patterns is by good trail design and construction, whereby a new trail has curvilinear alignment and modest grades (less than 10-15%). Such a trail should pass only through durable soils on hillsides that can sustain a well-compacted full bench and generous outslope. This facilitates sheet flow and minimizes the need for drainage structures.

## Slide 58: Curvilinear Layout Combined With Sidehill Construction and Outsloping Prevents Water Diversion and Accumulation

## Slide 59: Following the Contours of the Land Alone is not Sufficient for a Sustainable Trail
Notes: We need one more design concept to complete this picture of the ideal trail. Grade Reversals.

## Slide 60
Grade Reversals Must be Designed in Natural Drainages to Prevent Water Diversion
Notes: These pictures show how a water descending a natural drainage (aka draw, swale) can get diverted onto a trail. This could have been prevented with a grade reversal.

## Slide 61
Notes: The essence of the concept is that the trail should go uphill in both directions out of a natural drainage, no matter how dry or how small it seems.

## Slide 62
Notes: Despite the fact that this trail’s general trend is downhill at this point, it needs to climb uphill out of this drainage for just 10 feet or so, before continuing downward. That’s what we mean by reversing the grade temporarily.

## Slide 63: Grade Reversals are Sometimes Incorporated Even in the Absence of a Natural Drainage Crossing
Notes: Grade reversals are especially important wherever the trail passes through a natural drainage. However, as extra insurance, many designers incorporate frequent grade reversals even when the hillside is uniform, without apparent natural drainages. This is particularly pertinent under more erosive soil conditions, when the tread may not hold its outslope very well.

## Slide 64: Frequency of Grade Reversals or Drains Depends upon Trail Grade and Soil Type
Notes: Forest Service Trail Handbook chart suggesting spacing of grade reversals for specific soil types (because of their varying durability) for different trail grades.

## Slide 65: When Possible, Align above big Trees to minimize Resource Impacts and Trail Structures

## Slide 66: Retaining Walls are Usually Required When the Trail Passes Under a Large Tree
Notes: Without a retaining wall, trail builders would be cutting into the tree’s roots.

## Slide 67: Layout Trails on Hill Sides to Provide a Fuller Native Bench
Notes: Hill sides are better for trails than flat areas.

## Slide 68: Fuller Trail Benches Facilitate a Stable and Durable Trail Tread Surface

## Slide 69: Full Bench
Part Bench
Notes: Full bench construction means the entire tread surface rests on undisturbed native soil. Part bench means part of the tread surface is fill. Part bench is not recommended. The fill almost never becomes sturdy.

## Slide 70: Trails on Gentle Side Slopes With Part Bench do not facilitate Sheet Runoff as Efficiently
Notes: Trails can become difficult to drain when they are built on sideslopes of less than 15%. Only part-bench construction is possible when the sideslope is so gentle, and the sidecast material forms a berm that the water cannot surmount.

## Slide 71: Retaining the Landform’s Natural Drainage Patterns Is the Key to Sustainable Trails

## Slide 72: A Trail’s Tendency to Erode will be Influenced by many Factors. Consider these Factors in Order to Determine that Trail’s Maximum Sustainable Grade

## Slide 73: User Groups

## Slide 74
Source: Equestrian Trail Guidelines for Construction and Maintenance, published by the Conservation Commission of the State of Missouri
Notes: Each user type exerts a different kind of pressure and a different kind of wear upon a tread surface. It is important that trails are built with the right surface material and grade to withstand the user type for which they are intended.

## Slide 75
Level of Use
Notes: Heavier use usually means more erosion, therefore you’d want a gentler grade.

## Slide 76: Season of Use
Notes: This trail can withstand summer traffic much more than winter. If it is meant for winter use, consider making the grade more gentle.

## Slide 77: Soil Strength and Durability
Notes: This sandy soil does fine at a relatively flat grade, but as soon as the grade gets a bit steeper, it erodes.

## Slide 78: Annual Rainfall
Notes: How much water falls on the hillside?

## Slide 79: Rainfall Intensity
Notes: Also in this category would be rapid snowmelt. If a trail needs to withstand a lot of water all at once, that will affect what you deem to be the maximum grade.

## Slide 80: Canopy Cover
Notes: Can protect a tread surface from some erosion.

## Slide 81: Location on the Hillslope
Notes: See how much rainfall the trail must withstand based on its location on the hillslope. Higher is drier.

## Slide 82: Evaluate Existing Trails in the Area: Observe what Grade(s) are Sustainable
Notes: If possible, a designer should assess similar trails in the nearby area and observe what grades are sustainable there.
Based on all these factors and observations, a designer should determine the maximum sustainable grade for the new trail.

## Slide 83: Establish Prescribed Grade, then Compare to the Average Grade Between the Major Control Points
1,000 ft. elevation gain over 10,000 ft. of run
Notes: After you’ve established the maximum sustainable grade, go back to your map and look at the average grade between major control points.

## Slide 84: Rise ÷ Run = Grade Example: 1,000 Ft. Elevation Change ÷ 10,000 Ft. Linear Run = 10% Average Grade
Notes: How to determine grade.

## Slide 85: The Prescribed Linear Grade Is Used When Identifying Minor Control Points During Reconnaissance

## Slide 86: Elevations can be Taken with an Altimeter at each Control Point to Determine Elevation Differences

## Slide 87: Control Point Locations and Elevations are Plotted on a Topographic Map or GPS Unit

## Slide 88: Avoid Blind Flagging: It Often Results in Abrupt Grade Adjustments
landslide
rock outcrop
stream x
steep slopes
spring
Notes: For a given trail, while the overall target average grade may be 10%, the grade between any pair of control points is likely to vary. Make sure to work between two control points when ready to flag; otherwise, starting from the beginning and “blind flagging” at 10% will result in sudden grade adjustments as minor controls are encountered.

## Slide 89: Layout is Performed Between Control Points to Eliminate Abrupt Grade Changes
10%
8%
7%
9%
7%
6%

## Slide 90: Flagging From two Control Points Back Towards the Center is an Effective Method
10%
8%
7%
9%
7%
6%

## Slide 91
8%
7%
6%
9%
10%
9%
160’ elevation / 2,000’ of run = 8%
Notes: The average grade is 8%, but, some of the segments between control points are 10%. What to do if the maximum sustainable is 8%?

## Slide 92: If the Average Linear Grade Exceeds the Prescribed Grade Additional Linear Run may be Required
Notes: If the grade between two points exceeds maximum, a designer needs to add run (distance) with well-placed turns. Topographical turns are preferable to switchbacks or climbing turns, because they are less detectable, and therefore less prone to cutting.

## Slide 93: To Gain Additional Linear Run a Topographical Turn Should be Used First
Notes: If switchbacks or climbing turns are necessary, each one should be located very deliberately. Locate to facilitate drainage away from the corner by using a ridge nose or a natural topographical swale/drainage.

## Slide 96: If a Topographic Turn Is Not Available Then a Climbing Turn or Switchback Can Be Used to Gain Linear Run
<30%
>30%

## Slide 97: Climbing Turns and Switchbacks Need to Be Properly Placed
A Good Place for a Turn then becomes a Control Point
Notes: If switchbacks or climbing turns are necessary, each one should be located very deliberately. Ideal spots for turns are not easy to come by. Therefore, when a designer finds a good spot for a turn, that becomes a control point and influences trail alignment.

## Slide 98: Locate to Facilitate Drainage away from the Corner or Turn

## Slide 99: Use a Ridge Nose or a Swale/Drainage
Notes: Locate to facilitate drainage away from the corner by using a ridge nose or a natural topographical swale/drainage.

## Slide 100: There Must Be Good Separation Between the Two Legs to Prevent Cutting

## Slide 101: Utilize Trees, Rocks and Brush to Provide a Barrier Between the Two Legs. Proper Location will help Reduce Linear Grades

## Slide 102: Incorporating Vistas into Switchback Corners will Help Prevent Cutting

## Slide 103: When Using Multiple Switchbacks Maximize the Distance Between Each Switchback to Eliminate “Stacking”

## Slide 104
Notes: What is done right in this switchback? Drainage, topographical bump and imported log provide barrier and separation between the two legs

## Slide 105
Common Design Mistakes
Notes: Students will recognize common design mistakes evident in many existing trails. Inadequate planning can result in the need later to realign sections at steep grades, or to decommission trails that erode too easily.

## Slide 106: Laying Out Trails on Top of Ridges Should Be Avoided
Notes: Traditionally, many trails were located on broad ridge tops, where views are great, but opportunities to drain the tread are scant. The problem with ridgeline trails is one species of the problem with fall line trails.

## Slide 107
Notes: See how much soil this ridgetop trail has lost. It is very difficult to drain this trail in its present location.

## Slide 108
Notes: An extreme case of ridgetop trail erosion.

## Slide 109: Place Trails on the Side of the Ridge and Cross Over at Saddles to Provide Alternate Views
Notes: Better to locate trails on a hillside, and cross over the ridgeline at a saddle to provide views in the other direction.

## Slide 110: Crossing Over at a Saddle

## Slide 111: Flat Poorly Drained Land Should be Avoided
Notes: Flat areas and meadows, too, have historically been popular places to locate trails. However, these locations too are destined for drainage problems.

## Slide 112
Notes: On a flat creekside, the trail intercepts the hillside’s water before it can reach the creek.

## Slide 113
Notes: With any amount of compaction, a trail across a flat area becomes the lowest place on the landscape.

## Slide 114: Meadows and Open Prairies Should Be Avoided. Trail Alignments Should Skirt the Edges If Possible.
Notes: A trail cutting across a meadow can really change its hydrological patterns. It can even lower the water table and affect what kind of vegetation can survive there.

## Slide 115: Trail Flagging

## Slide 116: Prior to Flagging, Establish Horizontal Reference Points (“Zero”) on a Partner Using a Clinometer
Notes: After these slides are over, students should pair up with someone about their same height, and find Zero on that person while standing on flat ground.

## Slide 117: Sometimes there is too much height difference to establish a reliable reference point

## Slide 118
Notes: You can also use stakes with flags tied at the “Zero” reference point.

## Slide 119: With a Two Person Team The Shooter takes the Front Position so the Shooter Can See the Upcoming Terrain

## Slide 120: The Shooter Walks to a Location at the Approximate Prescribed Grade Staying on Contour

## Slide 121: The Shooter Locates Their Reference Point on their Partner and Moves up or Down Slope to the Prescribed Grade

## Slide 122: The Shooter Then Places a Flag Marking Trail Grade

## Slide 123: The Shooter Moves Forward for the Next Shot and the Partner Moves to Where the Shooter Previously Stood

## Slide 124: Be Careful Not to Shoot Across Topographic Features
Notes: When using a clinometer on variable terrain, be careful not to shoot across big bumps or depressions, as this will distort results.

## Slide 126: When Flagging in and out of a Stream, the Downhill Leg Needs to Level off or Climb for a Short Distance
Notes: Who remembers what this is called? A grade reversal.

## Slide 127: The Initial Flag Line Should Be Loose Flagged. Tight Flagging Is Performed Once the Loose Flagging Is Completed

## Slide 128: Finally, Make Note of any Special Trail Structures Needed

## Slide 129: Identify Potential Sources for Native Construction Materials
Notes: The end. Now you are ready for the trail construction crew!

## Slide 130: Trail Layout Process
Identify user types and design standards
Reconnaissance to evaluate the landform and soil
Observe hillside hydrological patterns
Determine maximum sustainable grade
Identify control points
Assess linear grades between controls
Incorporate well-placed turns if needed to decrease grade
Flag between control points
Develop plans for any trail structures
Notes: Review the Layout Process

## Slide 131: 200. Basic Trail Design